## Slide 1
Aliou Bamba, Ph.D,
Consultant en Télécommunications
BASES TECHNOLOGIQUES DES RÉSEAUX MOBILES : 2G, 3G, 4G, 5G

## Slide 2: Outline
Introduction
  Evolution des réseaux mobiles
  Caractéristiques de l’interface radio
  Architecture des réseaux mobiles
    Réseau de deuxième génération (GSM)
    Réseau GPRS/EDGE
    Réseau de troisième génération (UMTS)
    Réseau de quatrième génération (LTE)
  Cœur réseau avancées (IMS)
Conclusions

## Slide 3: Introduction
1G
AMPS TACS
NMT
2G
GSM D-AMPS
IS 95
3G
WCDMA/HSPA CDMA 2000
4G
LTE
5G
1980
1990
2000
2010
2020
The foundation of mobile telephony
Mobile telephony for everyone
The foundation of mobile broadband
Further enhanced mobile broadband
???

## Slide 4: Wireless Communication Systems
Transition from 2G to 3G (2.5G):
  Intermediate standards to 3G
  Motivation: Avoiding costs for new transmission technologies and infrastructure
  HSCSD (High Speed Circuit Switched Data)
  GPRS (General Packet Radio Service)
    New Core Network (routing)
    Importance of IP and internet access

## Slide 5: Wireless Communication Systems
Transition from 2G to 3G (2.5G):
  EDGE (Enhanced Data for Global Evolution)
    GSM/GPRS upgrade (TDMA/FDMA)
    Modulation Enhancement (8-PSK, Phase Shift Keying)
    Attractive for operators which cannot afford a licence for the radio spectrum
    Possible data rate of 384 kbit/s

## Slide 6: Introduction to GPRS
1.1. What is GPRS ?
1.2. GPRS access interfaces and reference points
1.3. How is GPRS seen by external networks and GPRS users
1.4. Air interface resources
1.5. GPRS characteristics
1.6. Applications

## Slide 7: Introduction to GPRS
  It is an enhancement of GSM.
  Allocation to GPRS is done dynamically according to capacity on demand.
  GPRS is also allow for broadcast multicast and unicast services.

## Slide 8: Introduction to GPRS
Part of GSM phase 2+
General Packet Radio Service
  General -> not restricted to GSM use (DECT ?, 3rd generation systems ?)
  Packet Radio -> enables packet mode communication over air
  Service, not System -> existing BSS (partially also NSS) infrastructure is used
Requires many new network elements into NSS
Provides connections to external packet data networks (Internet, X.25)
Main benefits
  Resources are reserved only when needed and charged accordingly
  Connection setup times are reduced
  Enables new service opportunities

## Slide 9: 1.5. GPRS characteristics
GPRS uses packet switched resource allocation
  resources allocated only when data is to be sent/received
Flexible channel allocation
  one to eight time slots
  available resources shared by active users
  up and down link channels reserved separately
  GPRS and circuit switched GSM services can use same time slots alternatively
Traffic characteristics suitable for GPRS
  Intermittent, bursty data transmissions
  Frequent transmissions of small volumes of data
  Infrequent transmission of larger volumes of data

## Slide 10: GPRS architecture
2.1. Interfaces, reference points and network elements
2.2. Functional view on GPRS
2.3. Subscription of GPRS service
2.4. New network elements
  2.4.1. GGSN
  2.4.2. SGSN
  2.4.3. Other elements
  2.4.4. GPRS backbones
2.5. GPRS Mobile classes
2.6. MS multislot capabilities

## Slide 11: GPRS access interfaces and reference points
GPRS provides packet switched connections from MS to packet data networks (PDN)
Different operator’s GPRS networks are connected through Gp interface

## Slide 12: 2.1. Interfaces, reference points and network elements

## Slide 13: GPRS architecture and interfaces
MS
BSS
GGSN
SGSN
MSC
Um
EIR
HLR/
GR
VLR
PDN
Gb
Gn
Gi
SGSN
Gn
Notes: Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
GlobalRoamer (GR)

## Slide 14: GPRS protocol architecture
apps.
IP/X.25
LLC
GTP
MAC
radio
MAC
radio
FR
RLC
BSSGP
IP/X.25
FR
Um
Gb
Gn
L1/L2
L1/L2
MS
BSS
SGSN
GGSN
UDP/TCP
Gi
SNDCP
RLC
BSSGP
IP
IP
LLC
UDP/TCP
SNDCP
GTP
Notes: Sub-network dependent convergence protocol (SNDCP)
Base Station System GPRS Protocol (BSSGP)
Radio Link Control/Medium Access Control (RLC /MAC) protocol
GPRS Tunneling Protocol (GTP)

## Slide 15: 2.2. Functional view on GPRS

## Slide 16: Assignment of functions to general logical architecture

## Slide 17: Gateway GPRS Support Node
GGSN
Typically located at one of the MSC sites
One (or few) per operator
Main functions
  Interface to external data networks
  Resembles to a data network router
  Forwards end user data to right SGSN
  Routes mobile originated packets to right destination
  Filters end user traffic
  Collects charging information for data network usage
  Data packets are not sent to MS unless the user has activated the PDP address

## Slide 18: Serving GPRS Support Node
SGSN
Functionally connected with BSC, physically can be at MSC or BSC site
One for few BSCs or one (or few) per every BSC
One SGSN can support BSCs of several MSC sites
Main functions
  Authenticates GPRS mobiles
  Handles mobile’s registration in GPRS network
  Handles mobile’s mobility management
  Relays MO and MT data traffic
    TCP/IP header compression, V.42bis data compression, error control MS- SGSN (ARQ)
  Collect charging information of air interface usage

## Slide 19: Security: Based on GSM phase 2
Authentication
  SGSN uses same principle as MSC/VLR:
    Get triplet, send RAND to MS, wait for SRES from MS, use Kc
  MS can’t authenticate the network
Key management in MS
  Kc generated same way from RAND using Ki as in GSM
Ciphering
  Ciphering algorithm is optimized for GPRS traffic (‘GPRS - A5’)
  Ciphering is done between MS and SGSN
User confidentiality
  IMSI is only used if a temporary identity is not available
  Temporary identity (TLLI) is exchanged over ciphered link

## Slide 20: GPRS Attach
GPRS Attach function is similar to IMSI attach
  Authenticate the mobile
  Generate the ciphering key
  Enable the ciphering
  Allocate temporary identity (TLLI)
  Copy subscriber profile from HLR to SGSN
After GPRS attach
  The location of the mobile is tracked
  Communication between MS and SGSN is secured
  Charging information is collected
  SGSN knows what the subscriber is allowed to do
  HLR knows the location of the MS in accuracy of SGSN

## Slide 21: FROM 2G TO 3G

## Slide 22: Introducing UMTS
Third Generation – IMT-2000:
  IMT-2000 (International Mobile Telecommunications at 2000 MHz)
  A standard created by the ITU (International Telecommunications Union)
  Different standards grouped together, to support existing infrastructure
UMTS Characteristics
  Requirements:
    High data rates
    Flexible operating environments
    Spectral efficiency/capacity
    Multimedia services
    Packet data network and IP mobility
    Global roaming
    Quality of service
    Interoperability with 2G network

## Slide 23: UTRAN Technology - FDD
UTRA – FDD:
  Paired frequency bands
  Two 5 MHz bands, for uplink and downlink
  Duplex distance of 190 MHz
  Signal spreading (Channelization code)
  W-CDMA
  Transfer rate of 3.84 million symbols per second (Mcps)
  Primary technology for UMTS in Europe

## Slide 24: UTRAN Technology - TDD
UTRA – TDD:
  Unpaired frequency bands
  One single 5 MHz band
  Usage of time slots
    Configuration of symmetric services
    Configuration of asymmetric services
    Advantage for data transmissions
  One frame (10 ms) consists of 15 timeslots
  Signal spreading (Channelization code)
  W-CDMA combined with TDMA

## Slide 25: UTRAN Technology - TDD
Types of Cells and Base station to use them
  Cells will operate in a hierarchy overlaying each other
    Pico Cells will operate in a Time division Duplex (TDD) mode
      TDD mode will use the same frequency to send and receive with a time frame being allocated.
    All other cells will operate in Frequency Division Duplex (FDD) Mode
      FDD will operate in the same manner as GSM, with a different frequencies for the Uplink and Downlink

## Slide 26: UTRA – FDD (W – CDMA)
The Frequency Division Duplex (FDD) mode for UTRA uses wide band CDMA.
The radio frame consists of 15 time slots.
One radio time consists 38,400 chips with a duration of 10ms.
There are three physical channels that are used for data transmission.
Two are used for uplink and one is used for downlink.

## Slide 27: UMTS Specifications
Based on GSM standards
The 3G standard was written by the International Telecommunication Union (ITU)
    The standard was referred to as IMT-2000
Transfer rates:
    144 kbps – Satellite and rural outdoor, (i.e., macrocell, max speed of 500 km/h)
    384 kbps – Urban outdoor (i.e., microcell, max speed of 120 km/h)
    2048 kbps – Indoor and low range outdoor (i.e., picocell, max speed of 10 km/h)
Objective to provide fairly high-speed wireless communications to support multimedia, data, and video in addition to voice
Difficult to predict
  Actual distances and bandwidth depend on local conditions
Voice quality comparable to PSTN

## Slide 28: UMTS Specifications
Bit Error Rate (BER)
  Real-time applications: 10-3 to 10-7 with maximum constant delay: 20ms to 300 ms
  No real-time applications: 10-5 to 10-8 with maximum delay >= 150ms.
Spectrum: 1900 MHz-2025 MHz, and 2110 -2200 MHz
  FDD (macro- and micro- cells: uplink is from 1920 MHz to 1980 MHz, downlink is from 2110 MHz to 2170 MHz
  TDD (pico- cells: not divided by use of different frequency carriers (not suitable for large prop delays).

## Slide 29: UMTS Specifications
UMTS Advantages:
  Improved capacity (4 to 5 times higher compared with GSM)
  Variable bit rate
  Quick and secure connection establishment
  Breathing cells
  Improved signal to noise ratio
  Broadband spectrum
  Macro diversity

## Slide 30: UMTS Specifications
Voice quality comparable to PSTN
Uses a pair of 5 MHz channels
Symmetrical and asymmetrical data rates
Support for packet-switched and circuit-switched services
More efficient use of available spectrum
Support for variety of mobile equipment
Flexibility to allow introduction of new services and technologies
Frequency bands:
    Uplink: 1885-2025 MHz
    Downlink: 2110-2200 MHz

## Slide 31: UMTS Specifications
UMTS
  UMTS provides different types of Quality of Service (QoS)
  Offers voice and data services the same as EDGE
    Services offered will be classed into one of the following
    From these classes certain defined Quality of Service (QOS) specifications are guaranteed like packet delay time
Conversational | Streaming | Interactive | Background
Real-Time |  | Best-effort, guarantee of quality delivery | 
Voice | Streaming Video on Demand | Web Pages, network gaming | MMS, SMS, emails, downloading

## Slide 32
Quality of Service (QoS) is the ability of a network element (e.g. an application, host or router) to have some level of assurance that its traffic and service requirements can be satisfied.
Newer applications with multimedia content
Demands of convergence
More bandwidth ?
User perception of service quality can be translated to network flow parameters such as delay and delay variation.
Quality-of-Service: What, Why?

## Slide 33
QoS perceived by the user must be end-to-end.
Parameters defining QoS of a flow must be fewer and simpler.
QoS definition must be compatible with all kinds of applications.
Must be able to quantify and enforce.
Guidelines for providing QoS to users

## Slide 34
QoS attributes for Traffic Classes

## Slide 35
QoS Characteristics of UMTS Classes
Very important
less important
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
delay
throughput
retransmission
Conversational
Streaming
Interactive
Background

## Slide 36
UMTS is downward compatible to GSM technology but will be capable to offer advanced features beyond existing GSM systems
Up to 2 Mbit mobile packet data
Up to 384 Kbit mobile video
Fixed/mobile convergence of protocols
Switching platform based on GSM II+
Wide range of terminals: voice, data only, multimedia
Downward compatible to GSM networks
Coverage limited but roaming available
9.6 Kbit/s data, up to 112 Kbit/s with GPRS
Up to 64 Kbit/s mobile video with HSCSD
Services similar to ISDN
GSM switching platform
Primarily voice terminals, first organiser announced
No compatibility to other networks
Full coverage, worldwide roaming
UMTS
GSM
UMTS Technical features compared with GSM

## Slide 37: UMTS Specifications
Types of Cells and Base station to use them
  Cells will operate in a hierarchy overlaying each other
Satellite
Macro-Cell
Micro-Cell
Urban
In-Building
Pico-Cell
Global
Suburban

## Slide 38: UMTS Air Interface
Radio Interface
  UMTS uses Wideband-Code Division Multiple Access (W-CDMA)
    Also known as “IMT-2000 Direct Spread”
    Extremely complex algorithms
    Uses 10x the current 2G processing power!
    Modulation is done with Quadrature phase shift keying (QPSK)
      This encodes 2 bits with each change
    Supports two modes of operation
      Frequency Division Duplex (FDD)
      Time Division Duplex (TDD)
W-CDMA
  Operates in the same manner as the CDMA used in the US
    CDMA allows multiple users to communicate at the same time over the same frequency
      Each of the devices is given a “Chipping code” this is known by the device and the base station.
      This chipping code is then used to identify the signal and allows the BS to receive the signal
      The chipping code is used to adjust the frequency of data transferred during the transfer
      The essential point of CDMA is the use of power control

## Slide 39: UMTS Air Interface
W-CDMA:
  Signal coding:
    Non Return To Zero Transmission
    Signal bit combined with code pattern (chips)
    Every bit is substituted with the resulting pattern
      Increased data rate
      Increased need of bandwidth
      Band spreading

## Slide 40: WCDMA Air Interface
In UMTS, the UTRAN is used to keep the mobility management (MM) and connection management (CM) layers independent of the air interface radio technology
This idea is realized as the concepts of access stratum (AS) and nonaccess stratum (NAS)
  AS: functional entity that includes radio access protocols between the user equipment (UE) and the UTRAN (terminate here).
  NAS: includes core network (CN) protocols between the UE and the CN itself.
The NAS protocols can be kept the same, thus, the GSM’s MM and CM resources are used almost unchanged in 3G NAS.

## Slide 41: UMTS architecture (Release 99)
UTRAN
UE
CN
Iu
Uu
UTRAN (UTRA Network)
  Cell level mobility
  Radio Network Subsystem (RNS)
  Encapsulation of all radio specific tasks
UE (User Equipment)
CN (Core Network)
  Inter system handover
  Location management if there is no dedicated connection between UE and UTRAN

## Slide 42: UMTS Architecture
GSM/GPRS networks use Time Division Multiple Access (TDMA) and Frequency Division Multiple Access (FDMA) air interface transmission
UMTS networks use Wide-band Code Division Multiple Access (WCDMA), 2 modes of operation (Frequency Division Duplex (FDD) and Time Division Duplex (TDD))
Requires new radio access network (RAN) called UMTS Terrestrial RAN (UTRAN)
UTRAN introduces 2 new network elements:
    Radio Network Controller (RNC) equivalent to BSC
    Node B equivalent to BTS (extends service to multiple cells)

## Slide 43: UTRAN Architecture
Core Network
Iub
RNS
RNC
Node B
Node B
Iu
Iub
Iub
RNS
RNC
Node B
Node B
Iub
Iur
Iu
Notes: 7

## Slide 44: UTRAN Architecture
Core network
protocols
Core network
protocols
Non-access Stratum
Radio
Protocols
Radio
Protocols
lu
Protocols
lu
Protocols
Access Stratum
Uu-interface
Iu-interface
UE
UTRAN
CN

## Slide 45: UMTS – Architecture
UTRA Network - Universal Terrestrial Radio Access Network .
The UTRAN is connected to user equipment (UE) via a radio interface via Uu and via Iu interface the UTRAN communicates with core Network (CN).
It handles cell level mobility and comprises several Radio Network Sub system (RNS).
The functions of RNS include ciphering, deciphering hand over control, Radio resource management.
It contains functions for inter system hand over, gate ways to other system networks etc.,

## Slide 46: User Equipment
UMTS uses USIM which identifies the subscriber to the core network
USIM functions:
    Supports multiple user profiles
    Security
    User authentication
UE is attached to both packet-switched (data) and circuit-switched (voice) domains and can concurrently use both services

## Slide 47: Node B
Node B is the UMTS equivalent of a base station transceiver. It may support one or more cells, although in general only one cell one Node B.
Provide service to one or more cells
Can be physically located within existing GSM BTS
Uses WCDMA to connect to UE
Support both FDD and TDD modes
ATM switching between Node B and RNC
Monitoring quality & strength of connection and calculates frame error rates
Other functions include:
  Air transmission and reception, CDMA physical channel coding
  Modulation and demodulation, Closed loop power control
  Mapping of Node B logical resources onto hardware resources
  Uplink power control
  Reporting of uplink interference measurements and downlink power information
  Contains the air interface physical layer, performs many functions such as RF processing, modulations, coding, and so on.

## Slide 48: Radio Network Controller (RNC)
One RNC controls one or more Node Bs.
It may be connected via Iu interface to an MSC (IuCS), or to an SGSN via Iu (IuPS).
The interface between RNCs (Iur) is logical interface, and a direct physical connection does not necessarily exist.
An RNC is comparable to a base station controller (BSC) in GSM networks.

## Slide 49: Radio Network Controller (RNC)
RNC provides centralized control of node B elements
Interfaces are ATM-based
Radio Resource Management is distributed to the RNC (GSM RRM is performed in the core network)
Other RNC functions:
    Connection to User Equipment (UE), Soft handover
    Congestion control, Handover control
    Broadcast signaling, Ciphering
    Channel allocation, Call admission control
    Encryption / Decryption
    ATM switching and multiplexing , protocol conversion
    Radio Resource Control, Code Allocation
    Power control, Hand over control
    Management

## Slide 50: Core Network (CN)
The Circuit Switched Domain (CSD) comprises the classical circuit switched services including signaling.
Resources are reserved at connection setup and GSM components MSC, GMSC (Gate way Mobile Switching Network) and VLR are used.
The Packet Switched Domain (PSD) uses GPRS components SGSN and CGSN and connects to the RNS interface.

## Slide 51: Core network
The Core Network (CN) and thus the Interface Iu, too, are separated into two logical domains:
Circuit Switched Domain (CSD)
  Circuit switched service incl. signaling
  Resource reservation at connection setup
  GSM components (MSC, GMSC, VLR)
  IuCS
Packet Switched Domain (PSD)
  GPRS components (SGSN, GGSN)
  IuPS
Release 99 uses the GSM/GPRS network and adds a new radio access!
  Helps to save a lot of money …
  Much faster deployment
  Not as flexible as newer releases (5, 6)

## Slide 52: From Mobile Networks to UMTS Revolution (1/6)
GSM Network

## Slide 53: From Mobile Networks to UMTS Revolution (2/6)
VALUE ADDED Service Platform

## Slide 54: From Mobile Networks to UMTS Revolution (3/6)
GPRS Service

## Slide 55: From Mobile Networks to UMTS Revolution (4/6)
3GPP R99 Network

## Slide 56: From Mobile Networks to UMTS Revolution (5/6)
3GPP R4 Network

## Slide 57: From Mobile Networks to UMTS Revolution (6/6)
3GPP R5 Network

## Slide 58: UMTS Radio Access Network (1/7)

## Slide 60: Core network: protocols
MSC
RNS
SGSN
GGSN
GMSC
HLR
VLR
RNS
Layer 1: PDH, SDH, SONET
Layer 2: ATM
Layer 3: IP
GPRS backbone (IP)
SS 7
GSM-CS
backbone
PSTN/
ISDN
PDN (X.25),
Internet (IP)
UTRAN
CN

## Slide 61: UMTS protocol stacks (user plane)
apps. &
protocols
MAC
radio
MAC
radio
RLC
SAR
Uu
IuCS
UE
UTRAN
3G
MSC
RLC
AAL2
ATM
AAL2
ATM
SAR
apps. &
protocols
MAC
radio
MAC
radio
PDCP
GTP
Uu
IuPS
UE
UTRAN
3G
SGSN
RLC
AAL5
ATM
AAL5
ATM
UDP/IP
PDCP
RLC
UDP/IP
UDP/IP
Gn
GTP
GTP
L2
L1
UDP/IP
L2
L1
GTP
3G
GGSN
IP, PPP,
…
IP, PPP,
…
IP tunnel
Circuit
switched
Packet
switched

## Slide 62: UMTS Core Network (1/2)

## Slide 63: UMTS Core Network (2/2)
end-to-end Services

## Slide 64: Spreading and scrambling of user data
Constant chipping rate of 3.84 Mchip/s
Different user data rates supported via different spreading factors
  higher data rate: less chips per bit and vice versa
User separation via unique, quasi orthogonal scrambling codes
  users are not separated via orthogonal spreading codes
  much simpler management of codes: each station can use the same orthogonal spreading codes
  precise synchronization not necessary as the scrambling codes stay quasi-orthogonal
data1
data2
data3
scrambling
code1
spr.
code3
spr.
code2
spr.
code1
data4
data5
scrambling
code2
spr.
code4
spr.
code1
sender1
sender2

## Slide 65: Orthogonal Spreading Variable Factor Coding
1
1,1
1,-1
1,1,1,1
1,1,-1,-1
X
X,X
X,-X
1,-1,1,-1
1,-1,-1,1
1,-1,-1,1,1,-1,-1,1
1,-1,-1,1,-1,1,1,-1
1,-1,1,-1,1,-1,1,-1
1,-1,1,-1,-1,1,-1,1
1,1,-1,-1,1,1,-1,-1
1,1,-1,-1,-1,-1,1,1
1,1,1,1,1,1,1,1
1,1,1,1,-1,-1,-1,-1
SF=1
SF=2
SF=4
SF=8
SF=n
SF=2n
...
...
...
...

## Slide 66: Logical Channels in UTRAN
Broadcast Control Channel (BCCH)
Paging Control Channel (PCCH)
Dedicated Control Channel (DCCH)
Common Control Channel (CCCH)
Control Channel (CCH)
Dedicated Traffic Channel (DTCH)
Traffic Channel (TCH)
ODMA Dedicated Control Channel (ODCCH)
ODMA Common Control Channel (OCCCH)
ODMA Dedicated Traffic Channel (ODTCH)
Common Traffic Channel (CTCH)
Shared Channel Control Channel (SHCCH)

## Slide 67: Dedicated Physical Control CHannel (DPCCH)
The channel conveys physical layer control data.
The pilot is used for channel estimation.
The transport Format Combination Identifier (TFCI) specifies the channels transported with in the DPDCHs.
Signaling for slot handover is supported by Feedback Information Field (FBI)
The Transmit Power Control ( TPC ) is used for controlling the transmission power of sender.

## Slide 68: Dedicated Physical Data Channel (DPDCH )
The channel conveys user or signaling data
The spreading factor (SF) of this channel is vary from 4 to 256.
The data rates can offer this channel are : 960 kbits/s, 480,240,120,60,30 and 15 kbits / s.
Bandwidth used by the user equipment is wasted due to orthogonal variable spreading factor.

## Slide 69: Dedicated Physical Channel (DPCH)
The downlink time of DPCH multiplexes both control and user data.
A Physical Random Access Channel (PRACH) is used for this purpose.
Spreading factors between 4 and 256 are used.
After power on the User Equipment (UE ) has to perform the following steps during the search for a cell.

## Slide 70: Dedicated Physical Channel (DPCH)
Primary synchronization :
A UE has to synchronize with the time slot structure with the help of a 256 chip primary code.
Secondary synchronization :
UE is now synchronized with the frame structure.
Identification of the scrambling code :
To find the right code using a correlator.

## Slide 71: UMTS FDD frame structure
W-CDMA
1920-1980 MHz uplink
2110-2170 MHz downlink
chipping rate: 3.840 Mchip/s
soft handover
QPSK
complex power control (1500 power control cycles/s)
spreading: UL: 4-256; DL:4-512
0
1
2
12
13
14
...
Radio frame
Pilot
FBI
TPC
Time slot
666.7 µs
10 ms
Data
Data1
uplink DPDCH
uplink DPCCH
downlink DPCH
TPC
TFCI
Pilot
666.7 µs
666.7 µs
DPCCH
DPDCH
2560 chips, 10 bits
2560 chips, 10*2k bits (k = 0...6)
TFCI
2560 chips, 10*2k bits (k = 0...7)
Data2
DPDCH
DPCCH
FBI: Feedback Information
TPC: Transmit Power Control
TFCI: Transport Format Combination Indicator
DPCCH: Dedicated Physical Control Channel
DPDCH: Dedicated Physical Data Channel
DPCH: Dedicated Physical Channel
Slot structure NOT for user separation
but synchronization for periodic functions!

## Slide 72: UMTS TDD frame structure (burst type 2)
TD-CDMA
2560 chips per slot
spreading: 1-16
symmetric or asymmetric slot assignment to UL/DL (min. 1 per direction)
tight synchronization needed
simpler power control (100-800 power control cycles/s)
0
1
2
12
13
14
...
Radio frame
Data
1104 chips
Midample
256 chips
Data
1104 chips
Time slot
666.7 µs
10 ms
Traffic burst
GP
GP: guard period
96 chips
2560 chips

## Slide 73: Support of mobility: macro diversity
Multicasting of data via several physical channels
  Enables soft handover
  FDD mode only
Uplink
  simultaneous reception of UE data at several Node Bs
  Reconstruction of data at Node B, SRNC or DRNC
Downlink
  Simultaneous transmission of data via different cells
  Different spreading codes in different cells
CN
Node B
RNC
Node B
UE

## Slide 74: UMTS Radio Access Network
Macrodiversity:
RNC Changes:

## Slide 75: Support of mobility: handover
From and to other systems (e.g., UMTS to GSM)
  This is a must as UMTS coverage will be poor in the beginning
RNS controlling the connection is called SRNS (Serving RNS)
RNS offering additional resources (e.g., for soft handover) is called Drift RNS (DRNS)
End-to-end connections between UE and CN only via Iu at the SRNS
  Change of SRNS requires change of Iu
  Initiated by the SRNS
  Controlled by the RNC and CN
SRNC
UE
DRNC
Iur
CN
Iu
Node B
Iub
Node B
Iub

## Slide 76: Example handover types in UMTS/GSM
RNC1
UE1
RNC2
Iur
3G MSC1
Iu
Node B1
Iub
Node B2
Node B3
3G MSC2
BSC
BTS
2G MSC3
A
Abis
UE2
UE3
UE4

## Slide 77
WCDMA is used to spreading the data spectrum and hence increase the data rate;
Development of a variety of applications and services with different level of QoS, leading to four classes of services.
Mobile network of third generation is the foundation for broadband communications;
Introduction of PS domain in the CN;
Notion of QoS is addressed for the first time
Communication between network elements through the different interfaces
Conclusions